## Slide 1
Renewable Intermittency and Grid Investment Dynamics
The Role of Scarcity-Induced Battery Innovation in Vietnam
Toan T. Nguyen (Justin) | Advisor: Dr. Xavier Martin G. Bautista | Fulbright University Vietnam

## Slide 2
Presentation Roadmap
1. Motivation: The Agility Gap
2. Research Question & Contributions
3. Model Overview
4. Households & Production
5. Grid Reliability & Flexibility Assets
6. Scarcity-Induced Technological Change
7. Government & External Sector
8. Calibration Strategy
9. Transmission Channels
10. Impulse Response Analysis
11. The Reliability Valley
12. Variance Decomposition
13. Welfare Analysis
14. Policy Counterfactuals
15. Conclusion & Implications

## Slide 3
Motivation: The Agility Gap
Vietnam's PDP8 targets 73.5 GW of renewable capacity by 2030 (from ~22.8 GW in 2024)
Battery storage remains near zero despite a 14 GW PDP8 target
Grid transmission investment grew modestly from $0.6B to $3.2B (2015-2024)
This structural mismatch = the "agility gap":
- Private battery investment: agile, modular, responsive to market signals
- Public grid investment: sluggish, subject to planning delays & construction lags

## Slide 4
Research Question
How does the structural divergence between rapid renewable deployment and
slow flexibility accumulation affect macroeconomic outcomes in a developing economy?
Three core contributions:
1. Endogenous reliability function linking capital utilization to flexibility assets
2. Scarcity-induced technological change where innovation responds to reliability gaps
3. Distinction between agile private (battery) and sluggish public (grid) investment

## Slide 5
Position in the Literature
This Thesis Bridges:
Environmental DSGE (E-DSGE)
- Heutel (2012), Fischer & Springborn (2011)
- Airaudo et al. (2025): greenflation
- Missing: grid reliability, storage
Directed Technical Change (DTC)
- Acemoglu (2002), Acemoglu et al. (2012)
- Hassler et al. (2021): resource scarcity
- Missing: intermittency, storage innovation
Gaps in the Literature
Learning-by-Doing / Experience Curves
- Arrow (1962), Kittner et al. (2017)
- Way et al. (2022): battery cost curves
- Missing: scarcity signals as driver
Small Open Economy DSGE
- Schmitt-Grohe & Uribe (2003)
- Mendoza (1991), Neumeyer & Perri (2005)
- Missing: energy transition frictions

## Slide 6
Model Overview
Small Open Economy DSGE model calibrated to Vietnam
16 endogenous variables, 16 equations, 3 exogenous shocks
Key agents:
- Representative household: consumes, supplies labor, invests in capital
- Representative firm: CES production (value-added + energy)
- Government: fiscal rule for grid investment
Three shocks:
- Intermittency shock (epsilon_ren): AR(1), rho=0.85
- Battery price shock (epsilon_bat): AR(1), rho=0.90
- Grid implementation shock (epsilon_I): i.i.d.

## Slide 7
Households
Utility: E_0 sum beta^t [ log(C_t) - phi * L_t^{1+sigma_L} / (1+sigma_L) ]
Discount factor beta = 0.99 (quarterly, 4% annual real rate)
Budget constraint: C_t + I_p + P_bat*I_bat + B* + tau*Y = wL + R*K_p + (1+r*)B*_{-1}
Euler equation (capital): 1/C_t = beta * E_t[ ((1-tau)*alpha*Y_{t+1}/K_p + 1-delta_p) / C_{t+1} ]
Labor supply: (1-tau)(1-alpha)V_t = phi * C_t * L_t^{1+sigma_L}
Proportional tax tau = 1.43% creates a constant fiscal wedge
International bonds B* with debt-elastic interest rate premium

## Slide 8
Production Sector
Nested CES Technology
CES Final Output:
Y_t = [(1-omega_E)V_t^{s_E} + omega_E*bar{E}^{s_E}]^{1/s_E}
sigma_E = 0.6 (energy-VA complements)
Value-Added:
V_t = Z * (u_t * K_{p,t-1})^alpha * L_t^{1-alpha}
alpha = 0.35 (capital share)
Key Mechanism
Reliability channel:
- u_t in (0,1): fraction of capital that is
operational given grid conditions
- NOT a choice variable; reflects system-wide
power availability
- 3% reliability shortfall ≈ 1% TFP loss
Energy endowment bar{E} is fixed (PDP8 targets)

## Slide 9
Grid Reliability & Flexibility
Reliability constraint: u_t = 1 - exp(-psi * F_t / (phi_int * Vol_ren))
- u_t: capital utilization (grid reliability)
- F_t: total flexibility assets (batteries + grid)
- Vol_ren: renewable output volatility
- psi = 2.0: sensitivity parameter
- phi_int = 55.6: integration complexity
Flexibility CES bundle: F_t = [ mu*(A_bat*K_b)^{s_F} + (1-mu)*K_g^{s_F} ]^{1/s_F}
- rho = 0.4 (imperfect complements: rho < 1)
- mu = 0.16 (battery weight in bundle)
- K_b: battery capital; K_g: grid capital
- A_bat: battery technology level

## Slide 10
Scarcity-Induced Technological Change
Battery technology evolves endogenously:
A_{bat,t} = A_{bat,t-1} * [1 + eta_bat * chi * (u* - u_t) / u*]
Key parameters:
- eta_bat = 0.10: innovation elasticity (Popp, 2002 range: 0.05-0.35)
- chi in [0,1]: regulatory signal transmission
- u* = 0.97: reliability target
Mechanism:
- When reliability falls below target, innovation accelerates
- Zero innovation at u_t = u* (steady state)
- One-period delay: A_{bat,t} enters F_{t+1}
If chi -> 0 (suppressed prices), innovation channel collapses entirely

## Slide 11
Government & External Sector
Government
- Grid investment rule:
I_{grid,t} / bar{I}_{grid} = (u* / u_t)^{phi_grid}
phi_grid = 1.5 (responsiveness)
- Financed by fixed proportional tax:
tau = 1.43% of output
- Reactive: invests more when grid is stressed
External Sector
- Bond Euler: 1/C_t = beta * E_t[(1+r*_t)/C_{t+1}]
- Debt-elastic premium:
r*_t = bar{r} + phi_b*(exp(bar{B}*-B*_t) - 1)
phi_b = 0.039 (data-anchored estimate)
- Resource constraint:
Y_t = C_t + I_p + P_bat*I_bat + I_grid + (B*_t - (1+r*_{t-1})B*_{t-1})

## Slide 12
Calibration Strategy
Standard parameters: GSO national accounts, World Bank data
beta = 0.99 (4% annual real rate), alpha = 0.35, delta_p = 2.5% quarterly
Reliability parameters: Moment-matched to EVN data
u_ss = 97% (EVN grid availability target)
psi = 2.0, phi_int = 55.6 (identified from level + slope moments)
Innovation parameters: Empirical literature
eta_bat = 0.10 (Popp, 2002; Kittner et al., 2017)
chi = 1.0 baseline / 0.3 regulated counterfactual
External sector: Vietnam-specific data
phi_b = 0.039 (OLS on World Bank real rate + external debt/GNI, R^2=0.16)

## Slide 13
Steady-State Characterization
Output Y_ss = 1.0 (normalized); Utilization u_ss = 97.0%
Consumption share C_ss/Y_ss = 73.4%
Productive capital K_p,ss = 9.83; Labor L_ss = 0.33
Flexibility assets:
- Battery capital K_b,ss = 0.19
- Grid capital K_g,ss = 1.14
- Battery-to-grid ratio = 0.167
Investment flows:
- Battery investment I_bat,ss = delta_b * K_b,ss
- Grid investment I_grid,ss = delta_g * K_g,ss = 1.43% of Y_ss
Tax rate tau_ss = 1.43% = I_grid,ss / Y_ss
Balanced trade: B*_ss = 0

## Slide 14
Three Core Transmission Channels
Channel 1: Intermittency -> Reliability -> Output
epsilon_ren increases Vol_ren -> u_t falls -> effective capital contracts -> Y_t drops
Channel 2: Reliability Gap -> Investment (The Agility Gap)
u*/u_t > 1 -> I_bat rises (private, agile)
u*/u_t > 1 -> I_grid rises (public, sluggish through accumulation lags)
Channel 3: Reliability Gap -> Scarcity-Induced Innovation
u*/u_t > 1 -> innovation accelerates -> A_bat improves -> F increases -> u recovers
Conditional on regulatory transmission parameter chi

## Slide 15
Impulse Response: Intermittency Shock
A one-standard-deviation intermittency shock (sigma_ren = 0.12):
On impact:
- Reliability u_t falls by 1.30%
- Output Y_t drops by 0.53%
- Productive investment I_p falls by 3.5% (Euler amplification)
- Consumption C_t falls by 0.06% (international smoothing)
Agility Gap response:
- Both I_bat and I_grid rise by 1.95% proportionally
- But grid investment is 2.5x larger in absolute levels
- Battery technology A_bat improves by ~0.65% by quarter 10
Persistence: AR(1) with rho=0.85 -> half-life ~4.3 quarters

## Slide 16
The Reliability Valley
Deterministic simulation: VRE penetration 15% -> 50% over 100 quarters (25 years)
Key result: Sustained reliability shortfall emerges mid-transition
- Nadir at quarter 45: u_t drops to 81.3%
- 15.7 percentage points below the 97% target
- Implies ~1,640 hours/year of unmet demand
Causes:
- VRE deployment outpaces flexibility accumulation
- Battery investment constrained by global prices
- Grid investment limited by institutional inertia
Comparable severity to 2021 Texas winter storm, but sustained for years

## Slide 17
Forecast Error Variance Decomposition
Intermittency Dominates Output
Output (Y_t)
epsilon_ren: 95.4%
epsilon_bat: 5%
epsilon_I: negligible
Reliability (u_t)
epsilon_ren: 95.8%
epsilon_bat: negligible
Battery Prices Drive Storage Investment
Battery Investment (I_bat)
epsilon_ren: negligible
epsilon_bat: 100%
Grid Investment (I_grid)
epsilon_ren: 25%
epsilon_I (implementation): 82%
Consumption (C_t)
epsilon_ren: 85%
epsilon_bat: 11%

## Slide 18
Welfare Analysis
Methodology: Lucas (1987) compensating consumption variation
Baseline welfare cost: Delta_Lambda = 0.000569% of steady-state consumption
Key results:
- Suppressing scarcity signals (chi -> 0): welfare cost rises by 20%
- Higher battery weight (mu): lower welfare costs (more agile storage)
- Higher grid responsiveness (phi_grid): modest improvement
- Impatient households (beta = 0.98): higher welfare costs
Joint shock scenario (intermittency + battery price):
- Additional welfare cost of 0.0189%
- "Scissors effect": intermittency raises need for storage
while battery price shock raises its cost

## Slide 19
Policy Counterfactuals
Battery Subsidy (P_bat = 0.8)
- Valley depth improves from 15.7pp to 9.6pp
- 38.6% reduction in depth
- Valley still persists (duration unchanged)
Accelerated Grid Planning
- Valley duration shortens by 20%
- Recovery achieved by quarter 81
- Valley depth improvement is modest
Key insight: Neither policy alone eliminates the valley
Superadditivity:
- Joint gain from coordinated investment exceeds
sum of individual gains by 32.9%
- Confirms complementarity proposition (rho < 1)
- Battery + grid are imperfect complements ->
need coordinated investment in both

## Slide 20
Joint Shock Scenario: Perfect Storm
Simultaneous one-standard-deviation shocks:
epsilon_ren (intermittency) + epsilon_bat (battery price)
Results:
- Output falls by 0.51% (similar to baseline)
- Battery investment declines by 6.05% (vs. +1.95% baseline)
- Current account deteriorates (twin drain effect)
- Welfare cost rises by additional 0.0189% of consumption
Policy implication:
- During a perfect storm, the economy cannot self-correct
through the storage channel
- Strengthens case for strategic battery reserves or
long-term procurement contracts

## Slide 21
Key Findings & Policy Implications
1. The reliability penalty is a tangible macroeconomic friction
- 0.53% output loss from a one-standard-deviation intermittency shock
2. The agility gap is structurally asymmetric
- Battery investment: 100% driven by global price shocks
- Grid investment: 82% driven by domestic implementation shocks
3. Scarcity-induced innovation provides a persistent adjustment mechanism
- But strictly conditional on regulatory signal transmission (chi)
- Suppressing scarcity signals raises welfare costs by 20%
4. Battery and grid are imperfect complements
- Coordinated investment produces superadditive gains
- Neither alone solves the reliability problem

## Slide 22
Policy Recommendations for Vietnam
1. Market-based scarcity signals
- Real-time pricing, capacity payments, ancillary service remuneration
- Need chi -> 1 to activate the innovation channel
2. Coordinated flexibility investment
- Battery subsidies alone insufficient (global price exposure)
- Grid planning acceleration alone insufficient (institutional lags)
- Need both: coordinated approach with superadditive gains
3. Domestic battery manufacturing capacity
- Reduces external vulnerability to global price shocks
- Attenuates the "twin drain" on the current account
4. Competitive wholesale electricity market (VWEM/VREM)
- Enables price discovery for reliability
- Unlocks scarcity-induced innovation channel

## Slide 23
Limitations & Future Research
Current Limitations
- Exogenous renewable endowment
- Representative household (no distributional effects)
- First-order approximation (linearization)
- No fossil fuel phase-out dynamics
- No carbon pricing / CBAM
- No cross-border electricity trade
Extensions
- Nominal rigidities + monetary policy (greenflation)
- Deterministic transition path for renewables
- Heterogeneous agents (distributional impacts)
- Endogenous renewable capacity decisions
- Carbon pricing + border adjustment mechanisms
- Second-order solution for large shocks

## Slide 24
Thank You
Questions & Discussion
Toan T. Nguyen (Justin) t.nguyen@fulbright.edu.vn